## Slide 1
Silicon FF/TT/SS corners & impact on PDN
For FF/SS silicon to switch at same freq as TT:
FF/SS silicon need to follow same I-V curve as TT
FF silicon needs lower V_GS or V_DS
  ▼Vdd
  ▼Power  CfV2
  ▼I_D
SS silicon needs higher V_GS or V_DS
  ▲Higher Vdd
  ▲Power  CfV2
  ▲I_D
V_GS=0.75V
V_GS=0.77V
V_GS=0.73V
V_GS=0.75V
V_GS=0.75V
V_GS=0.77V
V_GS=0.73V
Fig. I_D vs. V_DS curve (or I-V curve) family for FF, TT, SS silicon, respectively
PDN impact
  3 sets of current profiles for FF/TT/SS, respectively (e.g., via scaling factors ?)
  PDN will be more challenging to SS
    Increased Vpp noise, due to higher dI/dt
    Less headroom to 825mV ceiling, due to higher Vdd
  Other comments
V_GS FF
V_GS TT
V_GS SS
V_DS
I_D
I_D, SS
I_D, TT
I_D, FF